## Slide 1: IPCC Guidelines for National GHG Inventories and Reporting for Forest land
Nalin Srivastava
IPCC National Greenhouse Gas Inventories Program
World Forestry Week/19th Committee on Forestry Sessions in Rome,
March 16-20, 2009
Rome
Notes: <number>

## Slide 2: Outline
IPCC Guidelines on national greenhouse gas inventories
Relevance of IPCC Guidelines in the context of UNFCCC
IPCC methodologies for estimation of emissions from land use and land use change
Data requirements for implementation of IPCC methods for Forest land
Role of NFMA in supporting national GHG inventories and REDD
Conclusion
Notes: <number>

## Slide 3: IPCC Guidelines for National Greenhouse Gas Inventories
Revised 1996 Guidelines -Land-Use Change and Forestry (LUCF)
2000 Good Practice Guidance and Uncertainty Management (GPG2000)
Good Practice Guidance for Land Use, Land-Use Change and Forestry (GPG-LULUCF)
2006 IPCC Guidelines for National Greenhouse Gas Inventories
Notes: <number>

## Slide 4: Evolution of IPCC Guidelines on Land Use and Land Use Change(1)
1996 IPCC Guidelines
  Agriculture and Land Use and Change and Forestry (LUCF) separate sectors
  Focus on the most important activities resulting in GHG emissions/removals
  Implicit assumption about estimating emissions and removals only over lands subject to human intervention
GPG2000 & GPG-LULUCF
  Specifically address good practice and uncertainty management in national GHG inventory development
  GPG-LULUCF re-organized all emissions and removals from land use activities into six broad land-use categories
  GPG-LULUCF first used managed land as a proxy for anthropogenic emissions
Notes: <number>

## Slide 5: Evolution of IPCC Guidelines on Land Use and Land Use Change(2)
2006 Guidelines
  Integration of Agriculture and LUCF/LULUCF sectors into ‘Agriculture Forestry and Land Use’ (AFOLU) to remove inconsistencies and double counting
  Retained the basic structure of GPG-LULUCF
  Retained and made more explicit the concept of managed land as a proxy for anthropogenic emissions and removals
  Improved guidance on HWP
  Further refinement of methods and improved defaults
Notes: <number>

## Slide 6: Relevance of IPCC Guidelines in the context of UNFCCC
UNFCCC and Kyoto Protocol require the parties to report their national greenhouse gas inventories using the IPCC Guidelines
GPG2000 and GPG-LULUCF are mandatory for the Annex I countries while Non-Annex I countries are encouraged to use them for reporting their GHG inventories to the UNFCCC
Decision 2/CP.13 of ‘Bali Action Plan’ encourages the use of the most recent (GPG- LULUCF) IPCC Guidelines as a basis for reporting greenhouse gas emissions from deforestation
Notes: <number>

## Slide 7: IPCC Methodologies for Estimation of Emissions from Land Use and Land Use Change
Notes: <number>

## Slide 8: Six Land Use Categories
Other land
Forest land
Settlements
Wetland
Cropland
grassland
Notes: <number>

## Slide 9: Emissions and removals from a land use category
Land remaining in the
same land use category
Land changed to the land use category
from other land use categories
Total emissions
from a land use category
Emissions/removals are reported under the final land use category
Notes: <number>

## Slide 10: Basic approach in IPCC Guidelines for land use and land use change emissions
C fluxes occur at widely varying spatial and temporal scales
Direct Measurement of C fluxes extremely difficult due to heterogeneity of terrestrial ecosystems and uncertainty in measurements
A practical first order approach makes two assumptions:
  Flux of C = changes in carbon stocks in carbon pools
  Change in carbon stocks can be estimated from land use and management at various points in time, their impacts on carbon stocks and the biological response to them
Notes: <number>

## Slide 11: Estimating Carbon Stock Changes
(a) Stock change method (b) Gain loss method
Can be used by countries with national inventory systems
Can be used by countries without national inventory systems
Notes: <number>

## Slide 12: C Pools in different land use categories
Living biomass
Countries can choose to account for HWP pool
Dead Organic Matter
Notes: <number>

## Slide 13: How does the carbon stock change add up?
Annual carbon stock changes for a stratum of a land use category:
Annual C stock changes for a land use category:
ΔCLUi = ΔCAB + ΔCBB + ΔCDW + ΔCLI + ΔCSO + ΔCHWP
ΔCLU = Σ ΔCLU i
Annual carbon stock changes from all land use categories:
ΔCAFOLU= ΔCFL + ΔCCL + ΔCGL + ΔCWL + ΔCSL + ΔCOL
Notes: <number>

## Slide 14: Data needs for estimating emissions/removals from land use and land use change
Data needs
Area or area change data
for a land use category
(Activity Data)
Information on associated
carbon stocks
(Stock change factors)
Notes: <number>

## Slide 15: Three methodological Tiers
IPCC Guidelines provide three methodological tiers varying in complexity to be chosen on the basis of national circumstances
Tier1 :
  Simple first order approach
  Use Coarse activity data from global datasets, simplifying assumptions, IPCC default parameters, large uncertainties
Tier 2:
  A more accurate approach
  more disaggregated activity data, country specific parameter values, smaller uncertainties
Tier 3:
  Higher order methods
  detailed modeling and/or inventory measurement systems driven by data at higher resolution and much lower uncertainties
Higher Tier methods (Tier 2&3)are required for key source categories, source or sink categories that contribute substantially to the overall national inventory level, trend or uncertainty
Notes: <number>

## Slide 16: Data Requirements for Implementation of IPCC Methods for Forest land
Notes: <number>

## Slide 17: Carbon stock information
Carbon stocks in the forest land vary by climate, soil, forest type, management practices, disturbance regime etc.
Simplest IPCC methods (Tier 1) use default data on carbon stocks on broad continental scales stratified by climate, eco-zone, forest type and continent and do not capture the differences due to human induced disturbances etc.
Notes: <number>

## Slide 18: Stratification for Tier 1 methods in IPCC Guidelines
Climate | Soil | Ecological Zone
Boreal Cold temperate dry Cold temperate wet Warm temperate dry Warm temperate moist Tropical dry Tropical moist Tropical wet | High activity clay Low activity clay Sandy Spodic Volcanic Wetland Organic | Tropical rainforest Tropical moist deciduous forest Tropical dry forest Tropical shrubland Tropical desert Tropical mountain systems Subtropical humid forest Subtropical dry forest Subtropical steppe Subtropical desert Subtropical mountain systems Temperate oceanic forest Temperate continental forest Temperate steppe Temperate desert Temperate mountain systems Boreal coniferous forest Boreal tundra woodland Boreal mountain systems Polar
Notes: <number>

## Slide 19: Higher Tier stratification scheme
More accurate (higher tier) methods require country specific data with a finer disaggregation of carbon stocks by:
  Climate
  Soil type
  Forest type
  Species
  Age class
  Elevation
  Degree of disturbance (primary, secondary, logged…)
  Management practices
Tier 2/3 data from national inventories and/or modeling approaches will likely be required for REDD estimations
Notes: <number>

## Slide 20: Data on area and area changes
The land use and land use change area should be disaggregated to match the carbon stock information
Area stratification scheme for Tier 1 methods is based on the classification scheme for the default Carbon stocks and other parameters given in IPCC Guidelines
Higher tier methods require finer level of area stratification to match the more disaggregated information on C stocks
Notes: <number>

## Slide 21: Three approaches for area change representation
Approach 1 | Approach 2 | Approach 3
Net area of land use for various land use categories; no tracking of land use conversions | Tracking of land use conversion on a non-spatially explicit basis | Tracking of land use conversion on a spatially explicit basis
Net-Net changes between categories | Gross-net changes between categories | Gross-net changes between categories & within categories
Notes: <number>

## Slide 22: Data sources
National sources
  National forest/ land use inventories
  Annual census (agricultural census, urban census etc.)
  Periodic surveys
  Remote sensing data
International sources
  IPCC Guidelines default data
  FAO data (FRA, FAO Yearbook of Forest Products etc.)
  International land cover data sets (IGBP/DIS, USGS, GLCF, CLC2000 etc.)
Notes: <number>

## Slide 23: Issues to be considered for data acquisition
Area data should adequately, consistently, completely and transparently represent the land use and land use transitions within the whole country
Classification scheme may differ from the national one
Spatial resolution of area data (MMU)
Classification accuracy and uncertainty
Time series availability
Notes: <number>

## Slide 24: Issues to be considered…(2)
Comprehensiveness (wall-to-wall/sampling)
Cost
Availability of consistent and reliable historical data on forest land area is essential for REDD
Notes: <number>

## Slide 25: Role of NFMA in Supporting National GHG Inventories and REDD
Notes: <number>

## Slide 26: Role of NFMA in supporting national GHG inventories and REDD
Accurate, robust and reliable information on forests and other land uses critical to UNFCCC GHG reporting, future REDD regime and other international processes
NFMA has the potential to respond effectively to the information needs of UNFCCC process and others
NFMA should support regular and consistent monitoring of C stocks, area and area changes of forestland and other land uses
Notes: <number>

## Slide 27: Role of NFMA…(2)
NFMA should help gather information of all C pools at a higher level of disaggregation to support higher tier methods
The data collection efforts and sampling intensity should aim at a level of reliability that can be applicable to higher tier methods and REDD requirements
NFMA should aim at creating and enhancing national technical and institutional capacity to undertake regular monitoring of forests and other land uses.
Notes: <number>

## Slide 28: Conclusion
IPCC methodologies give detailed methods with varying degrees of complexity for different national circumstances for estimation of national GHG emissions and removals and can potentially be applied to REDD
Reliable and consistent Information on C stocks and areas of land use and land use changes is essential for estimating national GHG emissions and removals and REDD
NFMA process can be fine-tuned to adequately respond to the increased data needs for UNFCCC processes
Notes: <number>

## Slide 29: Thank You IPCC Guidelines in all UN languages can be downloaded from www.ipcc-nggip.or.jp
Notes: <number>